Rfduino:

CPU	~5mA
Bluetooth	~5.5mA (@-20db) to 16mA(@+4db)

in ultra low power-mode: ~4uA

RGB-LED:

up to 5x5mA (due to limitations of current sinking capabilities of Rfduino)

Vibro-Motor:

~50mA, when active

Touch-Sensor:

~0.5mA

Sound-Board:

~0.5mA (standby) to ~40mA (playing sound)

Rough estimation for nonstop use (400mAh Lipo):
20mA(RFDUINO)+15mA(LED)+25mA(Vibro)+20mA(Sound)=80mA	18mA(RFDUINO)+5mA(LED)+15mA(Vibro)+10mA(Sound)=48mA
-> at least 5-8 hours

Rough estimation for standby use (400mAh Lipo):
0.004mA(RFDUINO)+0mA(LED)+0mA(Vibro)+0.5mA(Touch)+0.5mA(Sound)=1mA
1mA(RFDUINO)+0mA(LED)+0mA(Vibro)+1mA(Touch)+1mA(Sound)=3mA
->at least 5-17 days